## Slide 1: A Supervised Tensor Dimension Reduction-Based Prognostics Model for Applications with Incomplete Imaging Data
Chengyu Zhou
Joint work with Dr. Xiaolei Fang
Edward P. Fitts Department of Industrial and Systems Engineering
North Carolina State University

## Slide 2: Outline
Motivation and Challenge
Proposed Methodology
  Modeling construction
  Parameter estimation
  Closed-form solutions
Simulation and Case Studies
Summary

## Slide 3: Motivation
A growing trend of using image sensing techniques for condition monitoring as they are noncontact and contain richer information
A degradation image stream is an image stream that contains the degradation information of a system

## Slide 4: Objectives
Asset
Asset
Asset
Real-Time Signals
Historical
Signals

## Slide 5: Literature Review
 | Existing methods | Limitations
Deep Learning | Aydemir and Paynabar (2019) Yang et al. (2021) Dong et al. (2021) Jiang et al. (2022) …… | Only provide point estimates of failure times Cannot be used for subsequent decision-making analysis such as maintenance optimization
Statistical Learning | Liu, Yeo, and Kalagnanam (2016) Fang et al. (2019) …… | No guarantee for effective feature extraction Cannot work for missing data

## Slide 6: Challenges and Solution
Challenge I: Effective Feature Extraction
  Dimension reduction and TTF prediction are separate
  Extracted features may not be effective for TTF prediction
Challenge II: Missing Data
Fig. Complete Data Fig. Incomplete (missing) Data

## Slide 7: Challenges and Solution
Solution: Supervised Tensor Dimension Reduction-Based Prognostic Modeling with Incomplete Imaging Data
Advantages:
  Dimension reduction process is supervised by historical TTFs which guaranteed the effective feature extraction
  Work for both complete and incomplete degradation image streams
Step I(A). Supervised Low-Dimensional Tensor Subspace Detection
Step I(B). Feature Extraction
Step I. Supervised Dimension Reduction
Step II. Tensor Regression

## Slide 8: The Model
Tensor Dimension Reduction
(Feature Extraction)
LLS Regression
Historical Tensors
(image streams)
Low-Dimensional Features
Basis Matrices of the Low-Dimensional Tensor Subspace
Step I(A): Supervised Low-Dimensional Tensor Subspace Detection
LLS Regression includes a variety of TTF distributions, such as (log)normal, (log)logistic, smallest extreme value, and Weibull, etc., which cover most of the TTF distributions in reality.
Historical TTF

## Slide 9: The Model
Step I(B): Feature Extraction
Step II: Construct Prognostic Model
Basis Matrices from Step I(A)
Historical Tensors (image streams) of Asset m
Historical TTF of Asset m

## Slide 10: Parameter Estimation
Steps I(B) and II: No need to discuss
Step I(A): Supervised Low-dimensional Tensor Subspace Detection
  Reparametrize to be a block-convex problem
  Block Updating Algorithm
Step I(A). Supervised Low-Dimensional Tensor Subspace Detection
Step I. Supervised Dimension Reduction
Step II. Tensor Regression
Step I(B). Feature Extraction

## Slide 11: Parameter Estimation
Convergence Property: The block updating algorithm converges to a stationary point with any initialization.

## Slide 12: Closed-Form Solutions
When the TTF follows a Normal (or Lognormal) distribution, we have analytical solution for each of the sub problems
I. Complete Data
II. Incomplete (missing) Data
  II(A). Entry(Pixel)-wise missing
  II(B). Image-wise missing

## Slide 13: Closed-Form Solutions - I.Complete Data
I. Complete Data

## Slide 14: Closed-Form Solutions - I.Complete Data
I. Complete Data

## Slide 15: Closed-Form Solutions - II.Missing Data
II(A). Entry-wise missing: Any pixel of the image tensor can be missing

## Slide 16: Closed-Form Solutions - II.Missing Data
II(A). Entry-wise missing: Any pixel of the image tensor can be missing

## Slide 17: Closed-Form Solutions - II.Missing Data
II(A). Entry-wise missing: Any pixel of the image tensor can be missing

## Slide 18: Closed-Form Solutions – II. Missing Data
II(B). Image-wise missing

## Slide 19: Simulation Study
For system , its image stream, , is generated from the following heat transfer process:
Thermal diffusivity coefficient:
Noise: i.i.d. are added to each pixel

## Slide 20: Simulation Study
Sample size: 500 systems; image size ; 400 systems for training and the remaining 100 for test; the number of images for different systems are different (truncated by TTF)
Time-to-failure (TTFs)
Transform each image stream to a time series by taking the average pixel intensity of each image
The TTF is the time point that the time series signal crosses 23
Benchmark: Unsupervised Dimension Reduction Based Prognostic Modeling for Imaging Data (Fang et al., 2019)
Step I: Multilinear Principal Component Analysis (MPCA) (Lu et al., 2008)
Step II: LLS Regression

## Slide 21: Results (Simulation Study)
Our proposed method outperforms the two benchmarks under all data missing rates.
With the increase of missing rate, the performance of all the 3 models decreases.
‘MPCA_CV’ always outperforms ‘MPCA (97%)’ and the superiority increases with the increase of missing rates.
0% missing
10% missing

## Slide 22: Results (Simulation Study)
Our proposed method outperforms the two benchmarks under all data missing rates.
With the increase of missing rate, the performance of all the 3 models decreases.
‘MPCA_CV’ always outperforms ‘MPCA (97%)’ and the superiority increases with the increase of missing rates.
50% missing
90% missing

## Slide 23: Case Study
Experiments: degradation tests for rolling element bearings
Each image: pixels
Time-to-failure: minutes

## Slide 24: Results (Case Study)
0% missing
10% missing
Our proposed method outperforms the two benchmarks under all data missing rates.
With the increase of missing rate, the performance of all the 3 models decreases.
‘MPCA_CV’ always outperforms ‘MPCA (97%)’ and the superiority increases with the increase of missing rates.

## Slide 25: Results (Case Study)
50% missing
90% missing
Our proposed method outperforms the two benchmarks under all data missing rates.
With the increase of missing rate, the performance of all the 3 models decreases.
‘MPCA_CV’ always outperforms ‘MPCA (97%)’ and the superiority increases with the increase of missing rates.

## Slide 26: Summary and Conclusions
A Supervised Tensor Dimension Reduction-Based Prognostic Model was proposed
A general optimization algorithm was developed
Closed-Form solution when the TTF is from a Normal/Lognormal distribution was discussed
Simulation and case studies were performed
  The results indicated that the proposed supervised dimension reduction-based model outperformed unsupervised dimension reduction-based benchmarks in terms of both prediction accuracy and precision